## Slide 1: ES858 Web Parameter Update SOP

## Slide 2
Turn on the projector.
Wire the projector RJ45 to PC (Direct wiring w/o hub)
Configure the projector IP to 192.168.0.100 from OSD
Configure the computer IP with the same subnet as projector. (Refer to below)
Before Update

## Slide 3
Run 「ESxxx Series Tools.exe」
Select language
Factory IP : select「192.168.0.100」
Press「Submit」
Step 1

## Slide 4
Press「Scan」
「Device info」will be displayed after scanning to the device.
Step 2

## Slide 5
Press「update cfg」
Note : don't press 「Factory Setting」
Step 3

## Slide 6
Update completed (message show 「cfg upload....OK」)
Step 4