## Slide 1: LAN FW Upgrade SOP
English Version

## Slide 2
Turn on the projector.
Wire the projector RJ45 to PC (Direct wiring w/o hub)
Configure the projector IP to 192.168.0.100 from OSD
Configure the computer IP with the same subnet as projector. (Refer to below)
Before Download

## Slide 3
Step 1
Apply the IP ：http://192.168.0.100/firmwareUpdate.asp，in web browser to enter the update web page
Assign the file directory by clicking “browse” button (*dld)
Clicking「Update」button
1
2
3

## Slide 4
Step2
Wait download proceeding around 4 minutes until the device reboot page changed. 。If any error message appeared , please redo the process as previous page.

## Slide 5
Confirm FW version
Please reboot the projector after upgrading.
Apply the IP ：http://192.168.0.100 from web browser.
Check the LAN FW version under System Status page.