## Slide 1
Turn on the projector.
Wire the projector RJ45 to PC (Direct wiring w/o hub)
Configure the projector IP to 192.168.0.100 from OSD
Configure the computer IP with the same subnet as projector. (Refer to below)
LAN FW (1/4)

## Slide 2
enter address on web browser：http://192.168.0.100/firmwareUpdate.asp
select FW file(.dld file)
press「Update」button
1
2
3
LAN FW (2/4)

## Slide 3
Wait for upgrading finish, it will take about 4 minutes. When upgrade finish it will display “Device Reboot” page.
If it display “cannot display the webpage” error message, pleasse reboot projector then execute Step1 again.
LAN FW (3/4)

## Slide 4
after upgrade finish, reboot projector
enter：http://192.168.0.100 on web browser
confirm LAN FW version on System Status page
LAN FW (4/4)

## Slide 5
Turn on the projector.
Wire the projector RJ45 to PC (Direct wiring w/o hub)
Configure the projector IP to 192.168.0.100 from OSD
Configure the computer IP with the same subnet as projector. (Refer to below)
LAN Config (1/5)

## Slide 6
Run 「ESxxx Series Tools.exe」
Select language
Factory IP : select「192.168.0.100」
Press「Submit」
LAN Config (2/5)

## Slide 7
Press「Scan」
「Device info」will be displayed after scanning to the device.
LAN Config (3/5)

## Slide 8
Press「update cfg」
Note : don't press 「Factory Setting」
LAN Config (4/5)

## Slide 9
Update completed (message show 「cfg upload....OK」)
LAN Config (5/5)